## Slide 1: Digital Mobile Radio (DMR) Demo
Prerequisites

## Slide 2: DMR Demo
Need A DMR ID before Configuring Hotspot.
  Go To (https://radioid.net) RadioID
  Register Your Info To Request A DMR ID and NXDT ID (If Wanted)
  You Must Upload A Watermark Copy (Official Copy) Of You Amateur Radio License To Get A DMR ID.
  Could Take One Or Two Days To Get A DMR ID Once All Info Is Sent.

## Slide 3: DMR Demo
Once You Have A DMR ID, Go To https://brandmeister.network
  Register With Them And Once Registered Go To Self Care And Enter A Hotspot Security Password.
    NOTE: This Password Is Different Than Your Logon Password.

## Slide 4: DMR Demo
Go To TGIF Network And Register With Them If TGIF Is Wanted: TGIF Network
  Once Registered Go To User Security (Under Login) and Get A Hotspot Security Key. (Click On The Green Refresh Button. A Key Will Appear – This Is Your Hotspot Security Key
  NOTE: As With Brandmeister, The Hotspot Security Key Is Separate Than Your Login Password.

## Slide 5: DMR Demo
Download Needed Software And WPSD Image.
  Go To balenaEtcher - Flash OS images to SD cards & USB drives
    Download The Software For Your Computer (Windows, MAC OS, Linux).

## Slide 6: DMR Demo
Go To The WPSD Project - W0CHP.radio
  Download WPSD Image Compatible With Your Raspberry PI.
    Download Trixie OS If For Raspberry PI Zero 2W & Model 2, 3, 4 & 5 Platforms.
    Download Nano Pi Neo For Generic Nano PI Neo Hardware.

## Slide 7: DMR Demo
Nextion Screen Notes.
  Nextion Screens Need A Display Image
    Files Ending With .HMI Are Ready For Editing And Compiling.
    Files Ending With .TFT Are Compiled And Ready For Writing To Display. These Files Can’t Be Further Edited.
    Easiest Way To Write An Image To A Screen Is With A MicroSD Card.
      Card Should Be No Larger Than 16GB
      Card Should Be Formated in FAT32
      Load Only Image File To MicroSD – No directories or Other Files.

## Slide 8: DMR Demo
Nextion Screen Notes (cont).
    Insert MicroSD Card With Image Into Nextion Screen SD Card Slot and Power On Screen. Image Automatically Copied To Nextion Display.

## Slide 9: DMR Demo
First Time Login:
  Username: pi-star
  Password: raspberry

## Slide 10: DMR Demo
Use The Following For MMDVM Modem:
  Dual (Full Duplex): MMDVM_HS_Dual_Hat (DB9MAT, DF2ET & D07EN) for Pi (GP10)
  Single (Half Duplex): MMDVM_HS_Hat (DB9MAT & DF2ET) for Pi (GP10)

## Slide 11: DMR Demo
On With The Demo If There Are No Questions.